## Slide 1: Accuracy and Precision in Raspberry Pi 5’s Software-Reported Power Dissipation
Nilma Abbas, Jesper Nordentoft, and Maja Kirkeby

## Slide 2: The motivation and problem
Raspberry Pi 5’s on-board power measurements is accessible and lightweight: could fit classroom use or testing.
Is Raspberry Pi 5’s on-board power measurements accurate and precise under controlled CPU workloads?

## Slide 3: Why we do it
Energy efficiency is key to sustainable system development.
Educators and researchers need practical ways to link software load with hardware energy use.
Raspberry Pi 5 is affordable and accessible for teaching and reproducible research.

## Slide 4: What we do
Investigate energy consumption of Raspberry Pi 5 under controlled CPU stress.
Loads: fixed utilizations (0,25,50,75,100%) and sweeps (0–100% in steps of 10%).
Compare Pi’s on-board PMIC readings with external Siglent reference.

## Slide 5: What can we measure with RP5

## Slide 6: How we do it
Protocol: 20s idle rests, 80s fixed-load blocks (we use stress-ng percentage load for CPU).
Internal (Pi power logs): sampled at ~10 Hz (100 ms period).
This is fast enough to capture workload step changes (like your 20s/80s stress blocks), but it won’t resolve very short spikes (<100 ms).
External: Siglent programmable supply records reference power.
Siglent sampling frequency ≈ 2 Hz (one sample every ~0.5 s).
Analysis: mean, std, integrated energy, correlation, regression, Bland–Altman.
Notes: In our setup, the Raspberry Pi 5’s internal power logs are sampled at ~10 Hz (100 ms), which provides sufficient temporal resolution for controlled workload experiments but may be too coarse to capture very short bursts or transient spikes in power.

## Slide 7: Key Results
segment | cpu_load_% | Pi_energy_J | Pi_mean_W_via_int | Siglent_energy_J | Siglent_mean_W_via_int
idle0 | 0 | 31.617 | 395 | 153.15 | 1.914
load25 | 25 | 75.302 | 941 | 204.1 | 2.551
load50 | 50 | 93.825 | 1.173 | 225.75 | 2.822
load75 | 75 | 55.851 | 698 | 242.05 | 3.026
load100 | 100 |  |  | 255.45 | 3.193
load_% | Pi_mean_W | Siglent_mean_W | Abs_error_W | Rel_error_%
0 | 0.3957 | 1.9462 | -1.5505 | -79.67
25 | 0.9434 | 2.5682 | -1.6248 | -63.27
50 | 1.1749 | 2.862 | -1.6871 | -58.95
75 | 1.4039 | 3.0436 | -1.6397000000000002 | -53.87
100 |  | 3.2436 |  | 

## Slide 8: Key Results

## Slide 9: Current per CPU load
Notes: The boxplot reveals a regression-like trend where both Siglent and Raspberry Pi energy logger readings increase with CPU load

## Slide 10: CPU load to Current Prediction
Notes: The scatterplot shows that current increases with CPU load, with Energy Logger measurements (blue) -by the Raspberry Pi’s internal estimates- rising more steeply than the Siglent (orange), as indicated by the regression lines.

## Slide 11: Correlation current
Notes: Pearson’s correlation measures the strength and direction of a linear relationship between two continuous, normally distributed variables

## Slide 12: Key Results
Pi systematically underreports power by ~2–2.6 W across loads.
Correlation between energy logger and Siglent time series is strong positive (r ≈ 0.799).
Energy integration confirms same bias; no hidden compensation.

## Slide 13: Interpretation
As it is, 79.9% is not good enough for research
Could give a hint of the current ≈ teaching energy-efficiency (relative tracking).
The type of external measurement equipment may have reduced the correlation.
Absolute accuracy requires calibration or external meter.

## Slide 14: Takeaways for Students
Understand how software load maps to energy consumption.
Learn validation/calibration of measurement tools.
Simple lab protocol: run stress-ng, record Pi+Siglent, compare.
Foundation for sustainable computing education.

## Slide 15: Who
Nilma Abbas
Associate Professor at Zealand Academy of Technologies and Business
Master’s Degree in ICTE from the University of Aalborg in Copenhagen
Founder of Girls in IT Zealand